## Slide 1
UVM IPC
Inter-Process Communication

## Slide 2: The Need
Reference Module
Item
Item
Item
Agent
Device
Under
Test
Scoreboard
Sequence
Agent
config
The environment is built from many components.
There is a need to transfer data between them.

## Slide 3: TLM 1.0 Transaction level modelling
#77c6fc
#bbe3fe
#ddf1fe
#494949
#477797
Interface based communication
Prevent Coupling between components
Easy way to transfer packets
introduction
pull port
push port
fifo port
pass through
analysis port

## Slide 4
introduction
pull port
push port
fifo port
pass through
analysis port
The consumer start the transaction
Connection one to one
implements get()
use get()

## Slide 5
introduction
pull port
push port
fifo port
pass through
analysis port
The producer start the transaction
Connection one to one
use write()
implements write()

## Slide 6
introduction
pull port
push port
fifo port
pass through
analysis port
No dependence between the consumer and producer
Connection one to one
implements write()
implements get()
use get()
use write()

## Slide 7
introduction
pull port
push port
fifo port
pass through
analysis port
Transfer the packets going through it
The ports must be from the same type
implements write()
use write()

## Slide 8
introduction
pull port
push port
fifo port
pass through
analysis port
The producer start the transaction
Connection one to many
THE MOST FREQUENTLY USED PORT
use write()
implements write()
implements write()

## Slide 9: Example of ports
memory
Item
Reference Module
Scoreboard

## Slide 10: Example of ports
memory
Item
port.write( )
function void write( )
compare ( )
endfunction

## Slide 11
UVM config
data base
Easy way to share data (interfaces, values etc.)
Global, can be configured from anywhere to anywhere.
Need
UVM built in singleton global data base
Store data by tag and type
Has set and get methods
Solution

## Slide 12: Need
Easy way to share data (interfaces, values etc.)
Global, can be configured from anywhere to anywhere.
UVM built in singleton global data base
Store data by tag and type
Has set and get methods
Solution
UVM config
data base

## Slide 13: Example of DB
Agent
config

## Slide 14: Example of DB
Agent
bit:
“is_active” : 1
string:
“is_master” : “master”
time:
“clk_cycle_time” : 5ns

## Slide 15: Example of DB
bit:
“is_active” : 1
string:
“is_master” : “master”
time:
“clk_cycle_time” : 5ns
sequencer
monitor
driver

## Slide 16: git diff
Establish a constant protocol
Determined who initiate the transaction
The direction is constant
Takes development time to setup
Efficient
TLM
Global named variables
Every call requires a complex string operation
Used for initialization and occasional communication.
Not efficient
config db

## Slide 17: שאלות
Try learning more